## Slide 1: Context Aware Anomaly Detection in Automotive CAN Without Decoding
- Ravi Rajput

## Slide 2: Presenter
Ravi Rajput
Principal Architect Information Security– NeoTech Global PVT LTD
Cybersecurity Expert | Creator of AutoHackOS | DEFCON Village Organizer
Core Expertise:
  Telecom and Automotive Cybersecurity
  Vulnerability Research (Windows, Linux, ARM)
  Reverse Engineering & Advanced Penetration Testing.
Contributions:
  Developed AutoHackOS, a globally adopted automotive pentesting OS, launched at Black Hat
  Millions of downloads by researchers and OEM testers worldwide
  Recognized for tool innovation in vehicle telematics and firmware analysis.
Community Roles:
  Core Team member at DEFCON Telecom Village
  Speaking Engagements: Presented at DEFCON, BLACKHAT, HITB, Nullcon, HITCON and several Bsides Conferences.

## Slide 3: Agenda
CAN Bus Is Blind: Problems with Traditional Detection
Machine Learning Algorithms for CAN Anomaly Detection
No-Decoding Paradigm: Why It’s a Game Changer
Why LSTM and LSTM-VAE Are Game Changers
Intuition Behind LSTM
Working Mechanism: LSTM Autoencoder
Working Mechanism: LSTM Variational Autoencoder
Handling Uncertainty in Automotive Detection
Data Pipeline: From Raw Candump to Anomaly Score
Demo
Key Findings & Results
Deployment Possibilities
Q&A

## Slide 4: CAN Bus Is Blind: Problems with Traditional Detection
Legacy Design Limitations
  Designed for reliability, not security – no authentication, encryption, or integrity checks
  Broadcast architecture – every ECU receives every message (no source validation)
  No built-in support for access control or anomaly detection
Rule/signature-based IDS can only detect known patterns
No State Awareness
  ECUs treat packets statelessly; they cannot track sequences or state transitions
  Allows malicious actors to inject inconsistent states without triggering alerts

## Slide 5: Machine Learning Algorithms for CAN Anomaly Detection
Rely heavily on protocol decoding and fixed thresholds
Fail to detect contextual, timing-based or adaptive attacks
Machine Learning Approaches
  Supervised Learning (Needs Labeled Data)
    Challenge: CAN datasets rarely have labeled attack samples so better for forensics rather than detection
  Unsupervised Learning (No Labels Required)
    Ideal for CAN bus: assume "normal is dominant", anomalies are rare
Why Sequence-Based Models Excel?
  CAN is sequential and time-sensitive
  Anomaly ≠ one wrong message — it’s a break in context

## Slide 6: No-Decoding Paradigm: Why It’s a Game Changer
Problems:
  Each vehicle model = different structure, signal meaning, encoding
  Not scalable across fleet or vendors
Solution: No-Decoding Advantage
  Treats CAN Logs as Raw Time-Series Data
    Enables generic, protocol-agnostic anomaly detection
  Statistical Features That Work Without Decoding
    CAN ID frequency and burst patterns
    Payload byte entropy
    Timing deltas
    Sequence correlation
  LSTM/LSTM-VAE models can learn:
    What a normal sequence of CAN messages looks like
    When message frequency or byte composition drifts from the norm
  Autoencoders trained only on "normal" behavior reconstruct expected output → deviation = anomaly

## Slide 7: Why LSTM and LSTM-VAE Are Game Changers
LSTM Autoencoder: Learning Normal Sequences
  LSTM: Long Short-Term Memory network
    Stores past context in hidden states
    Learns patterns in message order, timing, value flow
  Autoencoder structure:
    Encoder: Compresses sequence → latent vector
    Decoder: Reconstructs sequence from latent vector
    High reconstruction error = anomaly
LSTM-VAE: Probabilistic Sequence Understanding
  Adds variational inference to standard AE
  Learns a latent distribution (μ, σ), not just fixed vector
  Enables:
    Confidence estimation on predictions
    Better generalization to subtle anomalies
    Uncertainty scoring for alert prioritization

## Slide 8: Intuition Behind LSTM
Why Standard Neural Nets Fail for Sequences?
  Feed-forward networks lack memory — treat each CAN frame as independent
  No understanding of sequence flow or time dependencies
  CAN traffic is inherently time-series → requires memory of past behavior
LSTM: Long Short-Term Memory Networks
  Maintain a cell state (c_t) that flows through time steps
  Use gates to control:
    What to forget (f_t)
    What to remember (i_t)
    What to output (o_t)

## Slide 9: Working Mechanism: LSTM Autoencoder
Overall Architecture
  Sequence-to-sequence model:
      Input sequence → Encoder → Latent vector → Decoder → Reconstructed sequence
  Trained to minimize reconstruction error (typically MSE)
Anomaly Detection
  During test:
    Feed new sequences into the model
    Compute reconstruction loss
  Threshold-based flagging:
    If error > threshold → Anomaly Detected
    Threshold can be tuned statistically (e.g., 95th percentile of training loss)

## Slide 10: Working Mechanism: LSTM Autoencoder
Input:
  Sequence of CAN frames, typically shaped as:
  [sequence_length × features], e.g., [10 frames × (CAN ID + 8 bytes + delta_t)]
Encoder (LSTM):
  Reads input sequence one timestep at a time
  Learns to compress the temporal behavior into a fixed-size latent vector (z)
  Captures long-term memory of valid transitions
Latent Representation:
  Encodes learned sequence behavior
  Acts as “memory snapshot” of what normal looks like
Decoder (LSTM):
  Reconstructs the original sequence from the latent vector
  Outputs one frame at a time, learning to predict next values based on context
Loss Function:
  Loss = Mean Squared Error (MSE) between input and output sequences
  Higher error = more likely the input was anomalous

## Slide 11: Working Mechanism: LSTM Variational Autoencoder
LSTM-VAE = LSTM AE + Probabilistic Inference
  Extends the LSTM Autoencoder by modeling latent variables as distributions
  Instead of a single latent vector → samples from z ~ N(μ, σ²)
  Enables uncertainty-aware reconstruction and better generalization
Loss Function = Two Parts
  Reconstruction Loss (MSE):
    Measures how well the sequence is rebuilt
  KL Divergence Loss:
    Measures how far latent distribution deviates from standard normal KL(N(μ, σ²) || N(0,1))
Final Loss = MSE + β * KL Divergence

## Slide 12: Working Mechanism: LSTM Variational Autoencoder
Input:
  Same as LSTM AE: sequences of CAN frames with timing + payload info
Encoder (LSTM):
  Outputs two vectors instead of one:
    μ (mean)
    σ (log variance)
  These define a Gaussian latent distribution
Latent Sampling:
  Use reparameterization trick to sample:
    z = μ + σ * ε, where ε ~ N(0, I)
  Introduces controlled noise to improve robustness
Decoder (LSTM):
  Takes sampled z and reconstructs the input sequence
  Learns to generate expected behaviour from distribution samples

## Slide 13: Handling Uncertainty in Automotive Detection
Why Uncertainty Matters in CAN Anomaly Detection
  Automotive networks are noisy and bursty (e.g., sudden speed/brake variations, diagnostic floods)
  Static thresholds cause false positives
  Need models that can express confidence, not just anomaly/no anomaly
How LSTM-VAE Tackles Uncertainty
  Learns a distribution of valid behaviour rather than a fixed pattern
  Produces a latent vector with mean (μ) and variance (σ²)
  Samples from z ~ N(μ, σ²) introduces variability → more tolerance to natural deviations
Real-world Use Cases
  Replay Attacks: same message, wrong timing → latent shift triggers KL spike
  Fuzzing: entropy and frequency violate both reconstruction and distribution
  Cross-ECU leakage: valid CAN IDs injected from wrong context → caught via sequence break

## Slide 14: Data Pipeline: From Raw Candump to Anomaly Score
1. Raw CAN Log Collection
  Logs captured using candump
  Two files used:
    normal.log → used for training
    attack.log → used for evaluation
2. Parsing & Cleaning
  Extract key fields:
    timestamp
    CAN ID (hex → int)
    Payload bytes (up to 8 bytes)
  Filter malformed or non-standard frames
  Calculate derived fields:
    delta_t = timestamp difference between messages
    Entropy = randomness in payload
    Frequency of CAN ID in sliding window

## Slide 15: Data Pipeline: From Raw Candump to Anomaly Score
3. Feature Engineering
  Construct sequence windows
  Input features:
    CAN ID
    byte_0 to byte_7
    delta_t
    Entropy
  Normalize inputs (MinMax or Z-score)
  Output shape:
    [num_sequences, sequence_length, num_features]
4. Model Training
  For LSTM Autoencoder:
    Train on only normal sequences
    Use reconstruction loss (MSE)
  For LSTM-VAE:
    Learn latent distribution N(μ, σ²)
    Use combined loss: MSE + KL Divergence

## Slide 16: Data Pipeline: From Raw Candump to Anomaly Score
5. Inference & Scoring
  Replay or attack sequences passed into trained model
  For each sequence:
    Compute reconstruction error
    Compute KL divergence (for VAE)
    Aggregate into an anomaly score
    Flag sequences with score > threshold
6. Post-Processing & Visualization
  Plot:
    Top 5 anomalous CAN IDs
    Anomaly score over time
    Byte-level entropy heatmap
    CAN ID frequency spikes

## Slide 17: Demo

## Slide 18: Key Findings & Results
CAN ID Anomalies:
  Unusual or previously unseen IDs during replay/fuzzing
  Rare IDs showing up with high frequency
Payload Entropy Spikes:
  Random or erratic byte patterns
  High entropy frames correlating with injected/fuzzed data
Timing Deviations:
  delta_t shifts—e.g., valid message at wrong time (replay)
  Sudden high-frequency bursts or dropped delays

## Slide 19: Deployment Possibilities
Lightweight & Flexible ML Models
Telematics Gateway Integration
Flash model into security-focused ECUs for on-board evaluation
Possible integration with:
  SIEM systems
  Vehicle Security Operations Centers (VSOC)
  Dashboard alerting tools

## Slide 20
Q&A

## Slide 21
Thank You 🙏
धन्यवाद 🙏
આભાર 🙏
@infosecravi
@frustratedresearcher